## Slide 1
컴퓨터 시스템
Parallelism
This material is reproduced based on
핵심 컴퓨터구조 및 운영체제 해설(최종언저, 예문사), Computer Organization and Architecture, 9ed(by William Stallings) and
Computer Architecture(by Behrooz Parhami),
Copyrights are reserved by corresponding authors.
© 2021 Computer System
Pipelining Concepts
Pipelining in the student registration process.
Registrar
ID photo
Pickup
Start
here
Exit
Approval
1
Cashier
2
3
4
5
Strategies for improving performance
– Use multiple independent data paths accepting several instructions that are read out at once: multiple-instruction-issue or superscalar
– Overlap execution of several instructions, starting the next instruction before the previous one has run to completion: (super)pipelined
© 2021 Computer System
파이프라인
명령어 처리 과정을 여러 단계로 세분화해서 동시에 서로 다른 작업들이 수행되도록 하여 병렬성을 높이는 기법
CPU의 프로그램 처리 속도를 높이기 위하여 CPU 내부 하드웨어를 여러 단계로 나누어 동시에 처리하는 기술
수행과정
파이프라인 유형
© 2021 Computer System
단일 파이프라인

## Slide 2
© 2021 Computer System
Pipelined Instruction Execution
Pipelining in the MicroMIPS instruction execution process.
Cycle 7
Cycle 6
Cycle 5
Cycle 4
Cycle 3
Cycle 2
Cycle 1
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Cycle 8 Cycle 9
Instr cache
Instr cache
Instr cache
Instr cache
Instr cache
Data cache
Data cache
Data cache
Data cache
Data cache
Time dimension
Task dimension
Instr 5 Instr 4 Instr 3 Instr 2 Instr 1
© 2021 Computer System
파이프라인 사용시 성능향상
© 2021 Computer System
파이프라인의 문제점
파이프라인의 근본적 문제점
  모든 명령어들이 파이프라인 단계를 모두 거치지는 않는다
  어떤 명령어는 오퍼랜드를 인출할 필요가 없으나 구조를 단순화하기 위하여
4단계의 파이프라인을 통과
  클럭 스피드는 가장 긴 파이프라인 단계를 기준으로 설정
구조적 문제점
  FI단계와 EI 단계가 동시에 기억장치를 사용할 경우 기억장치 충돌에 따른 지연시간
데이터 문제점
  이전 명령어의 실행 결과를 다음 명령어가 사용할 때 생기는 데이터 의존성에 따른 문제
제어 문제점
  분기(특히 조건분기)의 경우 미리 인출한 명령어를 사용할 수 없는 문제
© 2021 Computer System
Pipeline Stalls or Bubbles
Read-after-write data dependency and its possible resolution through data forwarding .
Cycle 6
Cycle 5
Cycle 4
Cycle 7 Cycle 8
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
$5 = $6 + $7
$8 = $8 + $6
$9 = $8 + $2
sw $9, 0($3)
Data forwarding
Instr cache
Instr cache
Instr cache
Instr cache
Data cache
Data cache
Data cache
Data cache
First type of data dependency
Cycle 1 Cycle 2 Cycle 3

## Slide 3
파이프 라인의 문제점
© 2021 Computer System
© 2021 Computer System
Second Type of Data Dependency
Read-after-load data dependency and its possible resolution through bubble insertion and data forwarding.
Cycle 1 Cycle 2 Cycle 3 Cycle 4 Cycle 5 Cycle 6 Cycle 7 Cycle 8
Data mem
Instr mem
Reg file
Reg file
ALU
Data mem
Instr mem
Reg file
Reg file
ALU
Data mem
Instr mem
Reg file
Reg file
ALU
sw $6, . . .
lw $8, . . .
Insert bubble?
$9 = $8 + $2
Data mem
Instr mem
Reg file
Reg file
ALU
Reorder?
© 2021 Computer System
Control Dependency in a Pipeline
Control dependency due to conditional branch.
Cycle 1 Cycle 2 Cycle 3 Cycle 4 Cycle 5 Cycle 6 Cycle 7 Cycle 8
Data mem
Instr mem
Reg file
Reg file
ALU
Data mem
Instr mem
Reg file
Reg file
ALU
Data mem
Instr mem
Reg file
Reg file
ALU
$6 = $3 + $5
beq $1, $2, . . .
Insert bubble?
$9 = $8 + $2
Data mem
Instr mem
Reg file
Reg file
ALU
Reorder? (delayed branch)
Assume branch resolved here
Here would need 1-2 more bubbl es
© 2021 Computer System
Data Dependencies and Hazards
Data dependency in a pipeline.
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Cycle 1 Cycle 2 Cycle 3 Cycle 4 Cycle 5 Cycle 6 Cycle 7 Cycle 8 Cycle 9
$2 = $1 - $3
Instructions that read register $2
Instr cache
Instr cache
Instr cache
Instr cache
Instr cache
Data cache
Data cache
Data cache
Data cache
Data cache

## Slide 4
© 2021 Computer System
When a previous instruction writes back a value computed by the ALU into a register, the data dependency can always be resolved through forwarding.
Resolving Data Dependencies via Forwarding
Cycle 7
Cycle 6
Cycle 5
Cycle 4
Cycle 3
Cycle 2
Cycle 1
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Cycle 8 Cycle 9
$2 = $1 - $3
Instructions that read register $2
Instr cache
Instr cache
Instr cache
Instr cache
Data cache
Data cache
Data cache
Data cache
© 2021 Computer System
When the immediately preceding instruction writes a value read out from the data memory into a register, the data dependency cannot be resolved through forwarding (i.e., we cannot go back in time) and a bubble must be inserted in the pipeline.
Certain Data Dependencies Lead to Bubbles
Cycle 6
Cycle 5
Cycle 4
Cycle 3
Cycle 2
Cycle 1
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Reg file
Reg file
ALU
Cycle 7 Cycle 8 Cycle 9
lw $2,4($12)
Instructions that read register $2
Instr cache
Instr cache
Instr cache
Instr cache
Data cache
Data cache
Data cache
Data cache
© 2021 Computer System
Pipeline Branch Hazards
Software-based solutions
Compiler inserts a “no-op” after every branch (simple, but wasteful) Branch is redefined to take effect after the instruction that follows it Branch delay slot(s) are filled with useful instructions via reordering Hardware-based solutions
Mechanism similar to data hazard detector to flush the pipeline Constitutes a rudimentary form of branch prediction:
Always predict that the branch is not taken, flush if mistaken
More elaborate branch prediction strategies possible
© 2021 Computer System
Branch Prediction
Predicting whether a branch will be taken
Always predict that the branch will not be taken
Use program context to decide (backward branch is likely taken, forward branch is likely not taken)
Allow programmer or compiler to supply clues
Decide based on past history (maintain a small history table); to be discussed later
Apply a combination of factors: modern processors use elaborate techniques due to deep pipelines

## Slide 5
© 2021 Computer System
A Simple Branch Prediction Algorithm
Fig. 16.6 Four-state branch prediction scheme.
Not taken
Predict taken
Predict taken again
Predict not taken
Predict
not taken again
Not taken
Taken
Not taken
Taken
Taken
Not taken
Taken
Example 16.1
L1: ----
L2: ----
----
br <c2> L2
----
br <c1> L1
20 iter’s
10 iter’s
Impact of different branch prediction schemes
Solution
Always taken: 11 mispredictions, 94.8% accurate
bit history: 20 mispredictions, 90.5% accurate
bit history: Same as always taken
© 2021 Computer System
Hardware Implementation of Branch Prediction
Fig. 16.7 Hardware elements for a branch prediction scheme.
The mapping scheme used to go from PC contents to a table entry is the same as that used in direct-mapped caches (Chapter 18)
Addresses of recent branch instructions
Target addresses
Low-order
bits used as index
Logic
From PC
History bit(s)
Incremented
PC
Next PC
0
1
Compare =
Read-out table entry
© 2021 Computer System
Advanced Pipelining
Instr cache
Instruction fetch
Function unit 1
Function unit 2
Function unit 3
Ope- rand prep
Instr decode
Retirement & commit stages
Instr issue
Deep pipeline = superpipeline; also, superpipelined, superpipelining
Parallel instruction issue = superscalar, j-way issue (2-4 is typical)
Stage 1 Stage 2 Stage 3 Stage 4 Stage 5 Variable # of stages Stage q2 Stage q1 Stage q
© 2021 Computer System
슈퍼 파이프라인

## Slide 6
© 2021 Computer System
슈퍼스칼라
© 2021 Computer System
슈퍼파이프라인-슈퍼스칼라
© 2021 Computer System
VLIW(Very Long Instruction Word)
© 2021 Computer System
Performance Improvement for Deep Pipelines
Hardware-based methods
Lookahead past an instruction that will/may stall in the pipeline (out-of-order execution; requires in-order retirement)
Issue multiple instructions (requires more ports on register file) Eliminate false data dependencies via register renaming
Predict branch outcomes more accurately, or speculate
Software-based method
Pipeline-aware compilation
Loop unrolling to reduce the number of branches
Loop: Compute with index i Increment i by 1 | Loop: | Compute with index i Compute with index i + 1
Go to Loop if not done |  | Increment i by 2 Go to Loop if not done

## Slide 7
© 2021 Computer System
Superscalar
Term first coined in 1987
Refers to a machine that is designed to improve the performance of the execution of scalar instructions
In most applications the bulk of the operations are on scalar quantities
Represents the next step in the evolution of high- performance general- purpose processors
Essence of the approach is the ability to execute instructions independently and concurrently in different pipelines
Concept can be further exploited by allowing instructions to be executed in an order different from the program order
© 2021 Computer System
Superscalar vs. Ordinary Scalar
© 2021 Computer System
Constraints
Instruction level parallelism
  Refers to the degree to which the instructions of a program can be executed in parallel
  A combination of compiler based optimization and hardware techniques can be used to maximize instruction level parallelism
Limitations:
  True data dependency
  Procedural dependency
  Resource conflicts
  Output dependency (WAW: Write after Write)
  Antidependency(WAR: Write after Read)
B = 3
A = B + 1
B = 7
© 2021 Computer System
Effect of Dependencies

## Slide 8
© 2021 Computer System
Branch Prediction
Any high-performance pipelined machine must address the issue of dealing with branches
Intel 80486 addressed the problem by fetching both the next sequential instruction after a branch and speculatively fetching the branch target instruction
RISC machines:
  Delayed branch strategy was explored
  Processor always executes the single instruction that immediately follows the branch
  Keeps the pipeline full while the processor fetches a new instruction stream
Superscalar machines:
  Delayed branch strategy has less appeal
  Have returned to pre-RISC techniques of branch prediction
© 2021 Computer System
Design Issues – Instruction vs. Machine level
Instruction level parallelism
  Instructions in a sequence are independent
  Execution can be overlapped
  Governed by data and procedural dependency
Machine Parallelism
  Ability to take advantage of instruction level parallelism
  Governed by number of parallel pipelines
© 2021 Computer System
Instruction Issue Policy
Instruction issue
  Refers to the process of initiating instruction execution in the processor’s functional units
Instruction issue policy
  Refers to the protocol used to issue instructions
  Instruction issue occurs when instruction moves from the decode stage of the pipeline to the first execute stage of the pipeline
Three types of orderings are important:
  The order in which instructions are fetched
  The order in which instructions are executed
  The order in which instructions update the contents of register and memory locations
Superscalar instruction issue policies can be grouped into the following categories:
  In-order issue with in-order completion
  In-order issue with out-of-order completion
  Out-of-order issue with out-of-order completion
© 2021 Computer System
Superscalar Instruction Issue and Completion Policies

## Slide 9
© 2021 Computer System
Organization for Out-of-Order Issue
© 2021 Computer System
Conceptual Depiction of Superscalar Processing
© 2021 Computer System
Pentium 4 Block Diagram
© 2021 Computer System
Assume that one bubble must be inserted due to read-after-load dependency and after a branch when its delay slot cannot be filled. Let  be the fraction of all instructions that are followed by a bubble.
Pipeline Throughput with Dependencies
q
(1 + q/ t)(1 + )
Pipeline speedup =
R-type | 44%
Load | 24%
Store | 12%
Branch | 18%
Jump | 2%
Example 15.3
Calculate the effective CPI for MicroMIPS, assuming that a quarter of branch and load instructions are followed by bubbles.
Solution
Fraction of bubbles  = 0.25(0.24 + 0.18) = 0.105
CPI = 1 +  = 1.105 (which is very close to the ideal value of 1)