## Slide 1
Computer Architecture
Cache Memory
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Key Characteristics of Computer Memory Systems
Characteristics of Memory Systems | 
Location Refers to whether memory is internal and external to the computer Internal memory is often equated with main memory Processor requires its own local memory, in the form of registers Cache is another form of internal memory External memory consists of peripheral storage devices that are accessible to the processor via I/O controllers Capacity Memory is typically expressed in terms of bytes Unit of transfer For internal memory the unit of transfer is equal to the number of electrical lines into and out of the memory module reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings) © 2013 Computer Organization and Architecture | 
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Method of Accessing Units of Data
Sequential access
Memory is organized into units of data called records
Access must be made in a specific linear sequence
Access time is variable
Direct access
Involves a shared read- write mechanism
Individual blocks or records have a unique address based on physical location
Access time is variable
Random access
Each addressable location in memory has a unique, physically wired-in addressing mechanism
The time to access a
given location is independent of the
sequence of prior accesses and is constant
Any location can be selected at random and directly addressed and accessed
Main memory and some cache systems are random access
Associative
A word is retrieved based on a portion of its contents rather than its address
Each location has its
own addressing mechanism and retrieval
time is constant independent of location or prior access patterns
Cache memories may employ associative access

## Slide 2
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Capacity and Performance:
The two most important characteristics of memory
Three performance parameters are used:
Access time (latency)
For random-access memory it is the time it takes to perform a read or write operation
For non-random-access memory it is the time it takes to position the read- write mechanism at the desired location
Memory cycle time
Access time plus any additional time required before second access can commence
Additional time may be required for transients to die out on signal lines or to regenerate data if they are read destructively
Concerned with the system bus, not the processor
Transfer rate
The rate at which data can be transferred into or out of a memory unit
For random-access memory it is equal to 1/(cycle time)
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Memory
The most common forms are:
Semiconductor memory
Magnetic surface memory
Optical
Magneto-optical
Several physical characteristics of data storage are important:
Volatile memory
  Information decays naturally or is lost when electrical power is switched off
Nonvolatile memory
  Once recorded, information remains without deterioration until deliberately changed
  No electrical power is needed to retain information
Magnetic-surface memories
  Are nonvolatile
Semiconductor memory
  May be either volatile or nonvolatile
Nonerasable memory
  Cannot be altered, except by destroying the storage unit
  Semiconductor memory of this type is known as read-only memory (ROM)
For random-access memory the organization is a key design issue
Organization refers to the physical arrangement of bits to form words
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Memory Hierarchy
Design constraints on a computer’s memory can be summed up by three questions:
How much, how fast, how expensive
There is a trade-off among capacity, access time, and cost
Faster access time, greater cost per bit
Greater capacity, smaller cost per bit
Greater capacity, slower access time
The way out of the memory dilemma is not to rely on a single memory component or technology, but to employ a memory hierarchy
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Memory Hierarchy - Diagram

## Slide 3
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Locality of reference
Abraham Silberschatz, Greg Gagne, and Peter Baer Galvin, "Operating System Concepts”, 9th ed, Chapter 9
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Cache and Main Memory
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Cache/Main Memory Structure
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Cache Read Operation

## Slide 4
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Typical Cache Organization
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Elements of Cache Design
Cache Addresses | 
Virtual memory Facility that allows programs to address memory from a logical point of view, without regard to the amount of main memory physically available When used, the address fields of machine instructions contain virtual addresses For reads to and writes from main memory, a hardware memory management unit (MMU) translates each virtual address into a physical address in main memory reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings) © 2013 Computer Organization and Architecture | 
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Logical and Physical Caches

## Slide 5
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Mapping Function
Because there are fewer cache lines than main memory blocks, an algorithm is needed for mapping main memory blocks into cache lines
Three techniques can be used:
Direct
The simplest technique
Maps each block of main memory into only one possible cache line
Associative
Permits each main memory
block to be loaded into any
line of the cache
The cache control logic interprets a memory address simply as a Tag and a Word field
To determine whether a block is in the cache, the cache control logic must simultaneously examine every line’s Tag for a match
Set Associative
A compromise that exhibits
the strengths of both the
direct and associative approaches while reducing their disadvantages
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Direct Mapping
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Direct Mapping Cache Organization
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Direct Mapping Example

## Slide 6
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Direct Mapping Summary
Address length = (s + w) bits
Number of addressable units = 2s+w words or bytes Block size = line size = 2w words or bytes
Number of blocks in main memory = 2s+ w/2w = 2s Number of lines in cache = m = 2r
Size of tag = (s – r) bits
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Fully Associative Cache Organization
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Associative Mapping Example
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Associative Mapping Summary
Address length = (s + w) bits
Number of addressable units = 2s+w words or bytes Block size = line size = 2w words or bytes
Number of blocks in main memory = 2s+ w/2w = 2s Number of lines in cache = undetermined
Size of tag = s bits

## Slide 7
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Set Associative Mapping
Compromise that exhibits the strengths of both the direct and associative approaches while reducing their disadvantages
Cache consists of a number of sets Each set contains a number of lines
A given block maps to any line in a given set
e.g. 2 lines per set
2 way associative mapping
A given block can be in one of 2 lines in only one set
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Mapping From Main Memory to Cache:
k-way set associative
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
k-Way Set Associative Cache Organization
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Set Associative Mapping Summary
Address length = (s + w) bits
Number of addressable units = 2s+w words or bytes Block size = line size = 2w words or bytes
Number of blocks in main memory = 2s+w/2w=2s Number of lines in set = k
Number of sets = v = 2d
Number of lines in cache = m=kv = k * 2d
Size of cache = k * 2d+w words or bytes Size of tag = (s – d) bits

## Slide 8
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
2-way Set Associative Mapping Example
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Varying Associativity Over Cache Size
Replacement Algorithms | 
Once the cache has been filled, when a new block is brought into the cache, one of the existing blocks must be replaced For direct mapping there is only one possible line for any particular block and no choice is possible For the associative and set-associative techniques a replacement algorithm is needed To achieve high speed, an algorithm must be implemented in hardware reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings) © 2013 Computer Organization and Architecture | 
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
The four most common replacement algorithms are:
Least recently used (LRU)
Most effective
Replace that block in the set that has been in the cache longest with no reference to it
Because of its simplicity of implementation, LRU is the most popular replacement algorithm
First-in-first-out (FIFO)
Replace that block in the set that has been in the cache longest
Easily implemented as a round-robin or circular buffer technique
Least frequently used (LFU)
Replace that block in the set that has experienced the fewest references
Could be implemented by associating a counter with each line

## Slide 9
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Write Policy
When a block that is resident in the cache is to be replaced there are two cases to consider:
If the old block in the cache has not been altered then it may be overwritten with a new block without first writing out the old block
If at least one write operation has been performed on a word in that line of the cache then main memory must be updated by writing the line of cache out to the block of memory before bringing in the new block
There are two problems to contend with:
More than one device may have access to main memory
A more complex problem occurs when multiple processors are attached to the same bus and each processor has its own local cache - if a word is altered in one cache it could conceivably invalidate a word in other caches
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Write Through vs. Write Back
Write through
Simplest technique
All write operations are made to main memory as well as to the cache
The main disadvantage of this technique is that it generates substantial memory traffic and may create a bottleneck
Write back
Minimizes memory writes
Updates are made only in the cache
Portions of main memory are invalid and hence accesses by I/O modules can be allowed only through the cache
This makes for complex circuitry and a potential bottleneck
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Line Size
When a block of data is retrieved and placed in the cache not only the desired word but also some number of adjacent words are retrieved
As the block size increases the hit ratio will at first increase because of the principle of locality
As the block size increases more useful data are brought into the cache
The hit ratio will begin to decrease as the block becomes bigger and the probability of using the newly fetched information becomes less than the probability of reusing the information that has to be replaced
Two specific
effects come into play:
Larger blocks reduce the number of blocks that fit into a cache
As a block becomes larger each additional word is farther from the requested word
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Multilevel Caches
As logic density has increased it has become possible to have a cache on the same chip as the processor
The on-chip cache reduces the processor’s external bus activity and speeds up execution time and increases overall system performance
When the requested instruction or data is found in the on-chip cache, the bus access is eliminated
On-chip cache accesses will complete appreciably faster than would even zero-wait state bus cycles
During this period the bus is free to support other transfers
Two-level cache:
Internal cache designated as level 1 (L1)
External cache designated as level 2 (L2)
Potential savings due to the use of an L2 cache depends on the hit rates in both the L1 and L2 caches
The use of multilevel caches complicates all of the design issues related to caches, including size, replacement algorithm, and write policy

## Slide 10
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Hit Ratio (L1 & L2) for 8 Kbyte and 16 Kbyte L1
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Unified Versus Split Caches
Has become common to split cache:
One dedicated to instructions
One dedicated to data
Both exist at the same level, typically as two L1 caches
Advantages of unified cache:
Higher hit rate
  Balances load of instruction and data fetches automatically
  Only one cache needs to be designed and implemented
Trend is toward split caches at the L1 and unified caches for higher levels Advantages of split cache:
Eliminates cache contention between instruction fetch/decode unit and execution unit
  Important in pipelining
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Intel CPU Cache Evolution
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Pentium 4 Block Diagram

## Slide 11
ure, 9ed(by W. Stallings)
reproduced based on Computer Organization and Architect
© 2013 Computer Organization and Archi
tecture
Intel Nehalem Architecture
(i-7 core in 2008)
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
ARM Cache Features
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
ARM Cache and Write Buffer Organization
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Summary
Characteristics of Memory Systems
Location
Capacity
Unit of transfer
Memory Hierarchy
How much?
How fast?
How expensive?
Elements of cache design
Cache addresses
Cache size
Mapping function
Replacement algorithms
Write policy
Line size
Number of caches
Image from http://www.promotionalpro.com/blog/

## Slide 12
Computer Architecture
Internal Memory
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Memory Cell Operation
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Semiconductor Memory Types
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
RAM (Random Access Memory)
Dynamic RAM (DRAM)
Made with cells that store data as charge on capacitors
Presence or absence of charge in a capacitor is interpreted as a binary 1/0
Requires periodic charge refreshing to maintain data storage
The term dynamic refers to tendency of the stored charge to leak away, even with power continuously applied
Static RAM (SRAM)
Digital device that uses the same logic elements used in the processor
Binary values are stored using traditional flip-flop logic gate configurations
Will hold its data as long as power is supplied to it

## Slide 13
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Read Only Memory (ROM)
Contains a permanent pattern of data that cannot be changed or added to No power source is required to maintain the bit values in memory
Data or program is permanently in main memory and never needs to be loaded from a secondary storage device
Data is actually wired into the chip as part of the fabrication process
Disadvantages of this:
  No room for error, if one bit is wrong the whole batch of ROMs must be thrown out
  Data insertion step includes a relatively large fixed cost
Programmable ROM (PROM) | 
Less expensive alternative Nonvolatile and may be written into only once Writing process is performed electrically and may be performed by supplier or customer at a time later than the original chip fabrication Special equipment is required for the writing process Provides flexibility and convenience Attractive for high volume production runs reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings) © 2013 Computer Organization and Architecture | 
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Read-Mostly Memory
EPROM
Erasable programmable read-only memory
Erasure process can be performed repeatedly
More expensive than PROM but it has the advantage of the multiple update capability
EEPROM
Electrically erasable programmable read-only memory
Can be written into at any time without erasing prior contents
Combines the advantage of non-volatility with the flexibility of being updatable in place
More expensive than EPROM
Flash Memory
Intermediate between
EPROM and EEPROM in both cost and functionality
Uses an electrical erasing technology, does not provide byte-level erasure
Microchip is organized so that a section of memory cells are erased in a single action or “flash”
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Typical 16 Mb DRAM (4M x 4)

## Slide 14
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Memory Organization Example (256 KByte)
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
1MByte Module Organization
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Interleaved Memory
Composed of a collection of DRAM chips
Grouped together to form a memory bank
Each bank is independently able to service a memory read oKrbwarnitkesrceaquen ssetrvice K requests simultaneously, increasing memory read or write rates by a factor
oIff cKonsecutive words of memory are stored in different banks, the transfer of a block of memory is speeded up
Error Correction | 
Hard Failure Permanent physical defect Memory cell or cells affected cannot reliably store data but become stuck at 0 or 1 or switch erratically between 0 and 1 Can be caused by: Harsh environmental abuse Manufacturing defects Wear Soft Error Random, non-destructive event that alters the contents of one or more memory cells No permanent damage to memory Can be caused by: Power supply problems Alpha particles reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings) © 2013 Computer Organization and Architecture | 

## Slide 15
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Error Correcting Code Function
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Hamming Error Correcting Code
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Layout of Data Bits and Check Bits
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Check Bit Calculation

## Slide 16
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Hamming SEC-DED Code
Advanced DRAM Organization | 
One of the most critical system bottlenecks when using high-pDeRrfoArMmance processors is the interface to main internal memory The traditional DRAM chip is constrained both by its internal architecture and by its interface to the processor’s memory bus A number of enhancements to the basic DRAM architecture have been explored: DRAM reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings) © 2013 Computer Organization and Architecture | 
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
SDRAM Read Timing
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Double Data Rate SDRAM (DDR SDRAM)
SDRAM can only send data once per bus clock cycle
Double-data-rate SDRAM can send data twice per clock cycle, once on the rising edge of the clock pulse and once on the falling edge
Developed by the JEDEC Solid State Technology Association (Electronic Industries Alliance’s semiconductor-engineering-standardization body)

## Slide 17
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
DDR SDRAM Read Timing
Cache DRAM (CDRAM) | 
Developed by Mitsubishi Integrates a small SRAM cache onto a generic DRAM chip SRAM on the CDRAM can be used in two ways: It can be used as a true cache consisting of a number of 64-bit lines – Cache mode of the CDRAM is effective for ordinary random access to memory Can also be used as a buffer to support the serial access of a block of data reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings) © 2013 Computer Organization and Architecture | 
reproduced based on Computer Organization and Architecture, 9ed(by W. Stallings)
© 2013 Computer Organization and Architecture
Summary
Semiconductor main memory
Organization
DRAM and SRAM
Types of ROM
Chip logic
Chip packaging
Module organization
Interleaved memory
Error correction
Hard failure
Soft error
Hamming code
Advanced DRAM organization
Synchronous DRAM
DDR SDRAM
Cache DRAM